## Slide 1: Comparing Chromatography Methods for Quantitative Analysis of Epinephrine Degradation
CHEM-488 Honors Capstone
Rayshell Torres-Santana
Dr. Kristina Stefaniak

## Slide 2: What is Chromatography?
Process for separating components of a mixture
Separation based on size, charge, polarity, solubility
Two phases – mobile and stationary

## Slide 3: Types of Chromatography
High-Performance Liquid Chromatography (HPLC)
    Mobile Phase: liquid
Gas Chromatography (GC)
    Mobile Phase: gas

## Slide 4: Why Study Epinephrine?
First-line medical treatment for anaphylaxis
Epinephrine autoinjector pens known as EpiPen
Degradation – extreme temperatures, UV, expiration date
Issues: short supply, costly, 18 month expiration
Project Goal: to determine if epinephrine degrades at different temperatures

## Slide 5: Epinephrine Study Design
EpiPen instructions suggest:
    Store at 20°C to 25°C
    Excursions permitted from 15°C to 30°C
    Do NOT refrigerate
Testing Temperatures: Freezer, Fridge, Room Temperature, 30-90°C
Compare Chromatography Methods: GC-MS versus LC-MS

## Slide 6: GC-MS
Shimadzu Gas Chromatograph-2010 Plus Triple Quad
Little literature research
Method development
    Each run: ~10 min
    Different methods tested: 31
Sample: 1 mg/mL L-adrenaline in 0.1% L-ascorbic acid solution, in methanol for volatility

## Slide 7: GC-MS

## Slide 8: GC-MS
Troubleshooting:
    Epinephrine accumulating before reaching column and detector
    Precision of data varied for same sample
    Manual cleaning of injection needle
    Manual sample injection

## Slide 9: LC-MS
Shimadzu Liquid Chromatograph Mass Spectrometer – 8030 Triple Quad
More literature research
Method Development
    Each run: ~ 5 min
    Different methods tested: 38
Sample: 1 mg/mL L-adrenaline in 0.1% L-ascorbic acid solution

## Slide 10: LC-MS

## Slide 11: LC-MS Quantification
Using 38th method developed
Standards: 0.1-1 mg/mL L-adrenaline in 0.1% L-ascorbic acid solution
    Instrument response vs. standard concentrations
    Determine unknown concentration

## Slide 12: Temperature Trials
Samples held in temperature environments for 1 hour

## Slide 13: Conclusion
LC-MS better method than GC-MS
Epinephrine degrades in fridge and at high temperatures
    Confirm pharmaceutical company’s temperature suggestions, especially if EpiPen is not being stored continuously at room temperature
Future Directions:
    Longer degradation trials – 1 hour, 2 hours, 3 hours, etc.
    Troubleshooting GC-MS
    L-adrenaline solutions versus EpiPen solution degradation

## Slide 14: Acknowledgements
Dr. Kristina Stefaniak
Radford Chemistry Department
Honors College
Office of Undergraduate Research and Scholarship
Audience

## Slide 15: References
https://gfycat.com/brightembellishedherring
https://khn.org/news/mylans-generic-epipen-a-price-break-or-marketing-maneuver/
https://www.shimadzu.eu/gc-2010-plus-high-end-gc
https://www.youtube.com/watch?v=h2Hvo9Tqn5w
https://www.chem.pitt.edu/sites/default/files/GCMSQuickGuide_Shimadzu.pdf